## Slide 1
Lindo Channel Recharge Feasibility
Vina GSA Stakeholder Advisory Committee
Meeting - March 25, 2026

## Slide 2: Agenda
Overview
Scope of Work
Physical Setting
Field Programs and What we Learned
Questions
Modeling
Takeaways
Next Steps
Questions

## Slide 3: Lindo Channel Recharge Feasibility Overview
Component 4 of Vina GSA Implementation Grant
Working with City of Chico and State Agencies
Assessing Feasibility of Increasing Natural Recharge Along Lindo Channel
Notes: Historically known as Sandy Gulch
8.5=mile seasonal flood channel
Functions as diverted branch of Big Chico Creek
Only receives water during winter months
Water diverted into channel from Big Chico Creek at Five Mile Diversion

## Slide 4
Overview
Notes: 1965 USACE Lindo Channel Improvement
Consisted of Five Mile Gate System
Lindo Channel Gate
Weir at Head of Sycamore Bypass- Connects Lindo Channel and Sycamore Creek

## Slide 5: Scope of Work
Develop Flow Thresholder
Water Rights, habitat, downstream beneficial users
Estimate Expected Recharge Yield
Evaluate Infrastructure or Stream Improvement Needs
Assess Percolation (Infiltration) Rates
Prepare Project Draft Implementation Plan
Assess Environmental and Regulatory Permitting Needs
Assess Operational requirements
Monitoring Program

## Slide 6: Physical Setting
Topography
Hydrology
Hydrogeology

## Slide 7: Field Programs
Designed to Understand How Water Flows From Lindo Channel To Groundwater.
Infiltration Tests
Flow Rates
Continuous Water Levels
Water Quality Testing

## Slide 8: Infiltration Tests
Maximum – 491 Feet per Day
Minimum – 13 Feet per Day
Average – 262 Feet per Day
Model used 24 Feet per Day

## Slide 9: Flow Rates
Manzanita Avenue | Cussick Drive | West Sacramento
827 cfs | 667 cfs | 529 cfs
Questionable Data due to High Flow Rates and Debris
Does show decrease in flows going downstream
Confirms groundwater recharge
Calculated Groundwater Recharge > 100 AFD

## Slide 10: Continuous Water Levels
Stilling Wells
Domestic Wells
Interactions Between Lindo Channel Water and Groundwater

## Slide 11
From May 2025 to September 2025 Water Levels Dropped 12 to 13 Feet
Water Levels Recovered to May 2025 Levels by February 2026
Water Levels in Domestic Wells Clearly Show Response to Water in Lindo Channel

## Slide 12
Hydrographs Definetly show groundwater is being recharged by water in Lindo Channel.
Using simple assumptions infiltration rates 4 to 62 feet/day
With same assumptions groundwater recharge when water flowing 31 to 992 acre-feet/day

## Slide 13: Water Quality
All wells Mg-HCO3 Water Type – Shallow Fresh Groundwater.
After Flow in Lindo Channel modest increase in HCO3 and slight reduction in SO4 – Consistent with recharge pulse
Slight NA+K increase – minor cation exchange – also supports recharge signal
Isotope data Supports Quick Infiltration of Lindo Channel Water in Shallow Groundwater

## Slide 14: Questions

## Slide 15: FLOW MODELING

## Slide 16: Approach
Ecological flows assessment (not described here)
Flood flow frequency analysis at BIC
Flow split two-dimensional numerical modeling at Big Chico/Lindo
Lindo Channel one-dimensional numerical modeling
Infiltration calculations
Concurrent hydrogeologic analysis
Source: CDEC

## Slide 17: Flood flow frequency analysis
BIC gage
28 years of record (1997-present)
HEC-SSP (Bulletin 17C)
Discharges for 1-, 2-, 5- and 10-year return periods
Log-Pearson III distribution vs. Gumbel distribution
Representative historical runoff event selected for each return period event for numerical modeling

## Slide 18: 2D flow split modeling
HEC-RAS
Two terrains: existing and as-built
Hydrology from HEC-SSP
Goal – determine flow distribution between Big Chico (main channel), Lindo (distributary) and overflow channel (Sycamore Bypass).
Source: City of Chico

## Slide 19: Lindo Channel 2D flow split model

## Slide 20: Flow split model Hydrographs
Chart: 10-yr Discharge down Lindo Channel - Existing vs As-built conditions
Chart: 2-yr Discharge down Lindo Channel - Existing vs As-built conditions
| 36526.041666666664 | 36526.083333333336 | 36526.125 | 36526.166666666664 | 36526.208333333336 | 36526.25 | 36526.291666666664 | 36526.333333333336 | 36526.375 | 36526.416666666664 | 36526.458333333336 | 36526.5 | 36526.541666666664 | 36526.583333333336 | 36526.625 | 36526.666666666664 | 36526.708333333336 | 36526.75 | 36526.791666666664 | 36526.833333333336 | 36526.875 | 36526.916666666664 | 36526.958333333336 | 36527 | 36527.041666666664 | 36527.083333333336 | 36527.125 | 36527.166666666664 | 36527.208333333336 | 36527.25 | 36527.291666666664 | 36527.333333333336 | 36527.375 | 36527.416666666664 | 36527.458333333336 | 36527.5 | 36527.541666666664 | 36527.583333333336 | 36527.625 | 36527.666666666664 | 36527.708333333336 | 36527.75 | 36527.791666666664 | 36527.833333333336 | 36527.875 | 36527.916666666664 | 36527.958333333336 | 36528 | 36528.041666666664 | 36528.083333333336 | 36528.125 | 36528.166666666664 | 36528.208333333336 | 36528.25 | 36528.291666666664 | 36528.333333333336 | 36528.375 | 36528.416666666664 | 36528.458333333336 | 36528.5 | 36528.541666666664 | 36528.583333333336 | 36528.625 | 36528.666666666664 | 36528.708333333336 | 36528.75 | 36528.791666666664 | 36528.833333333336 | 36528.875 | 36528.916666666664 | 36528.958333333336 | 36529 | 36529.041666666664 | 36529.083333333336 | 36529.125 | 36529.166666666664 | 36529.208333333336 | 36529.25 | 36529.291666666664 | 36529.333333333336 | 36529.375 | 36529.416666666664 | 36529.458333333336 | 36529.5 | 36529.541666666664 | 36529.583333333336 | 36529.625 | 36529.666666666664 | 36529.708333333336 | 36529.75 | 36529.791666666664 | 36529.833333333336 | 36529.875 | 36529.916666666664 | 36529.958333333336 | 36530 | 36530.041666666664 | 36530.083333333336 | 36530.125 | 36530.166666666664 | 36530.208333333336 | 36530.25 | 36530.291666666664 | 36530.333333333336 | 36530.375 | 36530.416666666664 | 36530.458333333336 | 36530.5 | 36530.541666666664 | 36530.583333333336 | 36530.625 | 36530.666666666664 | 36530.708333333336 | 36530.75 | 36530.791666666664 | 36530.833333333336 | 36530.875 | 36530.916666666664 | 36530.958333333336 | 36531 | 36531.041666666664 | 36531.083333333336 | 36531.125 | 36531.166666666664 | 36531.208333333336 | 36531.25 | 36531.291666666664 | 36531.333333333336 | 36531.375 | 36531.416666666664 | 36531.458333333336 | 36531.5 | 36531.541666666664 | 36531.583333333336 | 36531.625 | 36531.666666666664 | 36531.708333333336 | 36531.75 | 36531.791666666664 | 36531.833333333336
As-built Conditions | 0 | 283.852 | 309.729 | 335.116 | 361.719 | 410.903 | 479.61 | 556.985 | 660.257 | 775.585 | 877.936 | 1061.874 | 1232.76 | 1316.417 | 1350.243 | 1375.982 | 1427.494 | 1441.328 | 1412.708 | 1401.134 | 1380.5 | 1332.89 | 1268.062 | 1195.432 | 1129.695 | 1069.893 | 1013.145 | 965.722 | 903.325 | 856.072 | 811.589 | 770.72 | 739.947 | 720.305 | 684.922 | 663.519 | 639.748 | 613.802 | 589.825 | 573.794 | 555.116 | 545.221 | 532.086 | 523.452 | 514.097 | 511.429 | 511.427
Existing Conditions | 0 | 346.777 | 400.397 | 455.882 | 515.386 | 630.602 | 793.503 | 953.956 | 1129.119 | 1276.884 | 1390.216 | 1575.054 | 1720.809 | 1785.354 | 1813.065 | 1833.879 | 1874.097 | 1883.956 | 1860.141 | 1852.986 | 1835.403 | 1795.411 | 1739.385 | 1678.812 | 1623.545 | 1571.575 | 1519.918 | 1475.192 | 1411.686 | 1361.065 | 1309.678 | 1260.95 | 1223.172 | 1198.962 | 1149.663 | 1119.258 | 1085.119 | 1043.42 | 1002.873 | 974.016 | 938.534 | 919.241 | 893.391 | 875.814 | 856.462 | 850.972 | 850.967
66%
63% of upstream hydrograph is distributed to Lindo Channel
Existing Conditions
As-built Conditions

## Slide 21: 1D Lindo Channel modeling
1D HEC-RAS Model developed by others
1D modeling goal is to determine top width and wetted perimeter for each section along the channel between Highway 99 and the Big Chico confluence at each model time step
Area available for infiltration is:
A = RL* WP (or B)

## Slide 22: Infiltration calculations
Python script written to organize results from HEC-RAS
Volume = A Dt IR
Assumptions: no saturated soils, constant infiltration rate in space, constant infiltration rate in time, sufficiently low groundwater table, no anisotropy
Did not use other methods (i.e., Green-Ampt) which require calibration
Calculations use 1 inch/hour

## Slide 23: Results – 2-year, Existing Condition
Chart: Upstream Discharge vs Incremental Infiltration Volume - 2-year, as-built

## Slide 24: Results – 2-year, as-built
Chart: Upstream Discharge vs Incremental Infiltration Volume - 2-year existing

## Slide 25: Results – 2-year, existing vs. as-built
D=-0.067, 1867 ACFT
Chart: 2-yr Storm Cumulative Infiltration Volume, Existing vs As-built Conditions
Existing Conditions
As-built Conditions

## Slide 26: Takeways
Infiltration in-stream provides a valuable source of groundwater recharge
Modeling indicates in-stream diversions can substantially increase groundwater recharge when considering more frequent, lower discharge storm events
Modeling indicates that in-stream diversions of frequent events can infiltrate groundwater more efficiently than storage basins in some systems
Long infiltration times for small, frequent runoff events are more efficient for recharge design than scalping high volumes for large, less frequent runoff events**
Field Investigations and Monitoring support these findings

## Slide 27: Alternatives and Next Steps
Modification to Sycamore Bypass to allow temporary increases
Grading in Lindo Channel to create ponding for low flows
Storm drain improvements that prevent water from leaving watershed
Identify opportunities to divert sheet flow to Lindo Channel
Install permanent monitoring system with telemetry
Engage in multi-agency coordination and long-term permitting.